# Teensy_sPWM Reference
## Overview
This is a library for emulating pulse-width modulation on Teensy 2.0 and similar devices.
## How to use
Before doing anything else, you must call PWM_init(int Hz), specifying a value for Hz. This will set up the library and all necessary subsystems, with pulse-width set by the frequency you specify in Hz.
You must have a program loop, in which PWM_loop() must be called regularly to generate the pulses. It should be called as often as possible, such as in an idle loop.
## Functions
### int PWM_init(unsigned int Hz, char options)
Initializes Arduino library so functions like millis() and micros() can be used. Initializes variables that associate pin letters and numbers with their respective internal representations. Sets all pins to 0% PWM. Sets the pulse width to the corresponding length as specified by the Hz parameter. The parameter options is used to set various internal operating modes. Valid options are:
MAKE_UP_LOST_TIME – When enabled the system will attempt to make up for delays to power a pin from the last cycle during the next one, and will subtract excess time spent in a previous powered cycle from the next one.
### void PWM_loop(void)
This function is responsible for updating pin statuses and pulse regulation. It should be called very often, ideally from a loop that runs infinitely (unless you wish to disable PWM).
### int set_pin_PWM(char port, char pin, uint8_t pwmPercent)
Sets the PWM level for a given pin. port should be a letter between A and F representing the port letters on the Teensy. pin should be an integer between 0 and 7 representing the respective pin number on a given port. pwmPercent is the level of PWM and should be an integer between 0 and 100. The following line would set pin B3 to PWM level of 75 percent:
set_pin_PWM('B', 3, 75);

int set_pin_PWM_normalized(char port, char pin, float normPwm)
This function is identical to set_pin_PWM, except for the parameter normPwm. You can pass a floating point value from 0.0 to 1.0 in normPwm, representing values from 0 to 100 percent.
### int set_abstract_pin_PWM(uint8_t pin, uint8_t pwmPercent)
Sets the PWM level for a given abstractly numbered pin. pin should be an integer between 0 and the number of pins on your given device, representing the respective pin number of this functions numbering convention (0 starts at upper left and goes down, continues at bottom right upwards, and then inward to the left. TODO: link or include a diagram showing pin numbering for different devices). pwmPercent is the level of PWM and should be an integer between 0 and 100. The following line would set pin B7 to PWM level of 75 percent, as pin B7 is abstract pin number 4:
set_abstract_pin_PWM(4, 75);

int set_abstract_pin_PWM_normalized(uint8_t pin, float normPwm)
This function is the same as set_abstract_pin_PWM, except for the parameter normPwm. You can pass a floating point value from 0.0 to 1.0 in normPwm, representing values from 0 to 100 percent.

TODO: Write descriptions for other library functions...
Last updated 9/12/12